## Slide 1: Alternating Current Power Factor Monitoring and Correction: Progress Presentation
Bryan Underwood
Advisor: Prof. Gutschlag

## Slide 2: Power Factor
Power Factor is the ratio of the active power to the apparent power
P.F. = P/S
http://electrical-engineering-portal.com/how-reactive-power-is-helpful-to-maintain-a-system-healthy

## Slide 3: Power Factor (cont.)
Poor power factor is due to inductive loads such as induction motors in air conditioners and refrigerators
A very low power factor usually results in the power company charging more on a utility bill

## Slide 4: Standards
Ameren Illinois requires Residential (rate DS-1) and Non-Residential (rate DS-2, DS-3) to maintain a power factor of 0.90 while Non-Residential (rate DS-4) must maintain a power factor of 0.95
http://www.ameren.com/sites/aiu/Rates/Documents/AIel14rtds4.pdf
http://www.ameren.com/sites/aiu/Rates/Documents/AIel48rdimf.pdf

## Slide 5: Power Company Charges
Ameren and ComEd require corrective devices to be installed
http://www.ameren.com/sites/aiu/Rates/Documents/AIel4otsq.pdf
Pacific Gas and Electric (PG&E) charges 0.6% per percentage point below a power factor of 0.85 more on a utility bill
http://www.pge.com/includes/docs/pdfs/mybusiness/customerservice/energystatus/powerquality/power%20factor--revised-8-9-07.pdf

## Slide 6: Industry Averages
About 60% of load is electric motors
http://www.pge.com/includes/docs/pdfs/mybusiness/customerservice/energystatus/powerquality/power%20factor--revised-8-9-07.pdf
According to the U.S. Energy Information Administration (EIA), about 25,000 out of 200,000 companies, in the manufacturing industry, participate in PFC
http://www.eia.gov/emeu/mecs/mecs2002/data02/excel/table8.1_02.xls

## Slide 7: Power Factor Correction (PFC)
Usually done by capacitor banks
  Generate “negative” reactive power
http://accessscience.com/content/Reactive-power/802370

## Slide 8: Changes to Equipment
Hampden Type WRM-100 3-Phase Motor
220 V
1.4 A
1725 RPM
1/3 HP

## Slide 9: Changes (cont.)
SATEC PM172E-N 3-Phase Programmable Power Meter

## Slide 10: Software
SATEC Power Analysis Software V1.4 Build 5
Configure basic setup of meter, set trigger points, and view event logs and waveforms

## Slide 11: Other Equipment
Potter & Brunfield KRPA-11AG-120 Power Relays

## Slide 12: Current Progress
SATEC power meter used to measure power factor, active and apparent powers, line voltages and currents, and energize relay coils

## Slide 13: Progress (cont.)
Relay coils are energized from SATEC meter when the power factor drops below a certain point

## Slide 14: Current System

## Slide 15: Revised Schedule
2/28/2012 Determine value of capacitors needed and confirm power meter measurements
3/6/2012 Implement capacitors and further study SATEC software
3/13/2012
3/20/2012 Research methods of improving individual motor efficiencies with power factor correction installed
3/27/2012
4/7/2012
4/10/2012 Begin work on final project presentation and final paper
4/17/2012
4/24/2012
5/01/2012 Project presentation

## Slide 16: Questions?