## Slide 1
Project Description
Automated Industrial Wind Tunnel
The remote control system of the wind tunnel allows users to change angle and sensor position of objects in the wind tunnel. It also provides an interface for users to record data
A web server hosts the necessary application files so that a remote user can download them. The web server will also host web cams. This will give the users visual feedback in addition to the data they receive from the microcontroller
The system involved integrates the existing wind tunnel systems with an 8051 microprocessor which conveys data from the wind tunnel to a server machine.
The primary purpose is to provide the wind tunnel users with a system to both collect data and to control the wind tunnel.
Secondary purposes involve
  Learning and evaluating LabView as a programming basis
  Providing a remote control system for the wind tunnel allowing viewing, controlling, and recording data from the remote system.
LabView
Description: Used LabView 2010 to develop the application. LabView is a graphical programming application. It allows users to “draw” code. It uses many of the same concepts such as while and for loops. Case statements and other logic devices are easily employed.
Pros:
  Easy to read and determine purpose of programming
    Data types are color coded – similar to syntax highlighting
  Enables simple creation of VI’s or “functions” to coalesce code
  Creating graphical user interfaces is very simple
Cons:
  Graphical user interfaces are somewhat limited in variability
  Development program is restricted: viewing is limited in scope
  Loop and variable interoperability can cause frustration
Microprocessor
Java Server
The Java server runs on the local wind tunnel computer.
Communicates with the microcontroller via RS232;
Accepts TCP connections to allow local and remote clients to control the wind tunnel and to collect data
Sends and Receives data in string format to allow for variability in client software
The microprocessor relays information to the server machine and accepts commands
Sensor Inputs:
  Lift
  Drag
  Ambient Temperature
  Ambient Air Pressure
  Wind Tunnel Air Pressure
  Three Actuator Potentiometers
Control Outputs:
  Main Blower On/Off
  Damper Open/Close (Wind Speed Up/Down)
  Actuator Position (Closed loop control of
    actuator based on potentiometer reading)
Safety precautions coded into the programming of the microcontroller to prevent damage to both the microcontroller and associated circuitry and to objects in the wind tunnel
System
Previous Work
Benjamin Morrison and Michael Firman (2010)
  Performed system analysis and purchased H-bridges and Solid State Relays
  Set up associated H-bridge circuitry
Adam Greene (2011)
  Rewired H-bridges and added power resisters to help protect power dissipation
  Added National Instruments D/A converter to communicate with PC – Required PCI LabView Card and specific machine
  Developed microcontroller and labview software to work with the NI D/A converter
Work done by Nicholas Detrempe and Daniel Monahan Advised by Dr. Aleksander Malinowski