## Slide 1: Aerial Collision Avoidance System
Brad Bergerhouse, Nelson Gaske, Austin Wenzel
Dr. Malinowski
Notes: A

## Slide 2: Outline
Description
Rationale
Goals
Hardware Subsystems
Software Subsystems
Results
Notes: B

## Slide 3: Description
Implement collision avoidance system on a quadcopter platform
Use minimal sensor input to accomplish avoidance
IR rangefinders and Camera input used for obstacle detection
Notes: N

## Slide 4: Rationale
Aerial Project
New project for department
Push our Linux knowledge
Complex System
Notes: B

## Slide 5: Goals
Use various sensors to detect obstacles
Autonomously avoid obstacles in the path
Eliminate collisions due to human error
Notes: A

## Slide 6: Hardware Systems
Xaircraft X650 Platform
BeagleBoard-xM
IR range finders
Battery and power system
Camera for Image Processing
Notes: A

## Slide 7: Block Diagram
Notes: B

## Slide 8: XAircraft X650 Quadcopter Platform
Notes: N

## Slide 9
Notes: N

## Slide 10: Rotor Guards
Notes: N

## Slide 11: BeagleBoard-xM
Includes TI OMAP DM3730 Processor
USB, I2C and serial communication interfaces
SD Card storage
Notes: A

## Slide 12: IR Range Finders
Sharp GP2Y0A02YK0F Sensors
Effective Range 15-150cm
Supply Voltage: 5V
Output Voltage: 0-3V
Notes: N

## Slide 13: IR Range sensor interpolation
Chart: Voltage Vs. Distance
| 15 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150
ADC input | 2.75 | 2.53 | 2 | 1.53 | 1.25 | 1.1 | 0.9 | 0.8 | 0.7 | 0.65 | 0.6 | 0.55 | 0.51 | 0.46 | 0.45
Notes: B

## Slide 14: Battery and Power System
Thunder Power 11.1V 3S 5000mAh LiPo
5V switching regulator
Notes: N

## Slide 15: Camera for Image Processing
Leopard imaging LI-LBCM5M1
5 Megapixel
Parallel input
Notes: A

## Slide 16: RC PWM
Pulses at 50Hz
High time 1ms to 2ms
Remaining cycle low voltage
Requires high precision and low jitter
Notes: B

## Slide 17: Software Systems
Angstrom Linux on the BeagleBoard
Real-time Xenomai subsystem
I2C sensor interface
Image Processing
Notes: B

## Slide 18: Angstrom Linux
Lightweight Linux distribution
Designed for embedded systems
Prebuilt and configured image
Compatible with Beagleboard-xM hardware
Notes: B

## Slide 19: Real-time Xenomai Framework
Set of patches for Linux kernel
Enables real-time kernel features
Provides framework for accurate timing
Necessary for precise timing in PWM generation
Notes: B

## Slide 20: I2C interface
1.8V logic on BeagleBoard
5V logic on ADC Board
Level converter used to interface
Notes: N

## Slide 21: Image Processing
Images captured via camera
Pixel information is transferred in parallel
DSP core processes pixel information
Processed pixels are sent to ARM core
Notes: A

## Slide 22: Color Distance
Calculate a pixel’s distance from a given color
Pixel color is updated in relation to distance
Brighter pixels are closer and darker pixels are farther away
Notes: A

## Slide 23: Color Distance
Notes: A

## Slide 24: Results
Platform Design and Assembly
Sensor Interfacing
RC PWM
Image Processing
Power Distribution
Notes: N