## Slide 1: Autonomous Quadrocopter Proposal
Brad Bergerhouse, Nelson Gaske, Austin Wenzel
Dr. Malinowski

## Slide 2: Outline
Introduction
Goals
Project Description
Tests
Schedule

## Slide 3: Outline
Introduction
Goals
Project Description
Tests
Schedule

## Slide 4: What is a Quadrocopter?
A quadrocopter is an aircraft that is lifted and propelled by four rotors.

## Slide 5: Why is this technology important?
Quadrocopters are inherently stable platforms which share advantages with helicopters and airplanes, without the disadvantages
Microprocessor and DSP chip integration provides an powerful core while maintaining the low power usage of single chip processors

## Slide 6: Why this project?
To develop an autonomous vehicle with 6-DOF
Tackle challenges presented during 3 dimensional navigation with minimal sensors
Provides a unique opportunity to implement an aerial platform for use in future department projects and courses

## Slide 7: Outline
Introduction
Goals
Project Description
Tests
Schedule

## Slide 8: Goals
Implement backup fly-by-wire controls for safety and testing
Avoid obstacles using video and sensor feedback
Autonomously navigate through narrow passages using onboard sensors
Develop a quadrocopter platform for future senior projects

## Slide 9: Fly-by-wire
Remotely control quadrocopter with computer joystick or R/C transmitter for safety
Implemented to prevent loss of control during development and testing

## Slide 10: Obstacle Avoidance
Use range sensors and single camera to avoid obstacles
Range sensors will be (initially) positioned in all 6 Euclidian directions
Camera will be aimed forward and DSP will be used for object detection

## Slide 11: Autonomous Navigation
Navigate narrow passages in a fully autonomous nature
Create ‘obstacles’ using symbols to indicate directional constraints

## Slide 12: Future Platform
Fully document design process and component interfacing
Expandable processing and I/O components

## Slide 13: Outline
Introduction
Goals
Project Description
Tests
Schedule

## Slide 14: Project Description
Interface BeagleBoard with XAircraft X650 Quadrocopter platform
Use BeagleBoard I/O to interface with sensors and remote controls
Develop passage following algorithm using minimal sensor input
Utilize image processing techniques to detect obstacles or goal criteria

## Slide 15: System Diagram

## Slide 16: System Diagram

## Slide 17: XAircraft X650
Platform includes controllers, motors, and infrastructure required for operation
Accepts industry standard R/C PWM inputs for flight controller
Handles stability and individual motor control for arbitrary PWM inputs

## Slide 18: System Diagram

## Slide 19: BeagleBoard
Includes TI OMAP processor, USB interfaces and camera header
Performs processing required for navigation
Outputs industry standard PWM directly into flight controller

## Slide 20: System Diagram

## Slide 21: IR Distance Sensors
Output analog voltage based upon distance to an obstacle
Linear response between 10cm and 150cm
ADC necessary to interface with Beagleboard

## Slide 22: TI ADC
12-bit Octal ADC with I2C interface
Bridges logic between sensors and Beagleboard
50K samples per second

## Slide 23: System Diagram

## Slide 24: Accelerometer
Possibly used for orientation input to BeagleBoard

## Slide 25: System Diagram

## Slide 26: I2C Interface
Inter-Integrated Circuit
Master-slave 2-wire bus interface
Used to communicate between ADC, Accelerometer, and BeagleBoard
Additional logic level converter required to interface between BeagleBoard (1.8V) and ADC (5V)

## Slide 27: System Diagram

## Slide 28: Camera
Captures images, send to BeagleBoard over serial communication
5-Megapixel image output with downsizing for processing speed

## Slide 29: System Diagram

## Slide 30: Laptop
Communicates via 802.11 wireless protocol to BeagleBoard
Transmits manual override controls to Beagleboard
Provides goal conditions for navigation
Can act as a data store for retrieved information

## Slide 31: System Diagram

## Slide 32: DSP
Images processed using Canny edge detection algorithm
Symbol detection using predefined symbols for navigation control
Communicates with processor using shared memory regions

## Slide 33: System Diagram

## Slide 34: OMAP ARM core
Interprets sensor information
Provides control outputs to platform
Monitors sensor inputs for proper goal conditions

## Slide 35: Outline
Introduction
Goals
Project Description
Tests
Schedule

## Slide 36: Tests to be performed
Tethered Testing
  Takeoff and Landing
  Move at constant altitude to a landmark
  Change altitude during flight, continue to landmark
  Move in straight line through narrow passageway
Un-Tethered Testing
  Fly straight and return to starting position
  Fly through narrow passageway and turn corner

## Slide 37: Outline
Introduction
Goals
Project Description
Tests
Schedule

## Slide 38: Division of labor
Austin
  DSP and object recognition
Brad
  Communication and networking
Nelson
  Hardware interfacing and power management

## Slide 39: Schedule
11/17-Camera and Joystick Interfacing
12/1-Wireless and I2C interfacing
1/19-PWM output design
1/26-PWM output testing
2/2-IR sensor interfacing
2/9-Platform Assembly
2/16-Platform Power Testing
2/23-Initial Navigation Design

## Slide 40: Schedule contd
3/1-Navigation Design
3/8-Navigation Design
3/22-Navigation Design
3/29-Test Design
4/5-Testing and debugging
4/12-Testing and debugging
4/19-Testing and debugging
4/26-Presentation preparation

## Slide 41: Questions?