## Slide 1: Reconfigurable Patch Antenna
With Matching Network
Presented by: Mike Bly, Josh Rohman Advisor: Dr. Prasad N. Shastry

## Slide 2: Presentation Outline
Introduction to Reconfigurable Antenna
Alternative Options
Design Criteria
Patch Antenna Design
Switching Method and Implementation
Simulation
Matching Network
Schedule

## Slide 3: Reconfigurable Antenna?
One antenna system that supports multiple single frequency bands.
Types: Patch Antennas, Wire Antennas, PIFAs

## Slide 4: Alternative Option 1: Multiple Antennas
More Antennas = More Required Space
Single Band

## Slide 5: Alternative Option 2: Wideband Antenna
One antenna supports all frequency bands needed
Reduced space compared to multiple antennas, but large bandwidth
Noise from large bandwidth

## Slide 6: Proposed Design Criteria
Patch antenna on microstrip board
2 GPS application frequencies
  1.227 GHz
  1.575 GHz
Double stub impedance matching network
  Matched to 50Ω
MEMS preferred switching method

## Slide 7: Patch Antenna
Rogers Corporation RO3010 Microstrip Board
  εr = 10.2, h = 5 mils
1.227 GHz, 1.575 GHz
Right Hand Circular Polarization

## Slide 8: Patch Antenna
Equations:
  L1 = W = 2.988 cm
  L2 (total) = 3.795 cm
  dL2 = 0.807 cm

## Slide 9: Switching Method
MEMS Switch
  RMSW201, RADANT MEMS
  SPST
  DC to 20 GHz
  0.3dB Insertion Loss @ 2GHz
  35dB Isolation Loss @ 2GHz
  1.9mm x 1.85mm package size
  +/- 90V Gate-Source Voltage
  Wire bonding to board

## Slide 10: Switching Method
DC-DC Converter: +5V to -90V

## Slide 11: Implementing MEMS
Via holes to ground plane

## Slide 12: Implementing MEMS
Conductive epoxy over via hole
Wire bonding, gold plating

## Slide 13: Simulations: Linear Patch Antenna
PCAAD 6.0
Simulate Linear Patch Antenna (square or rectangle) to determine resonant frequency
Simulate both patches separately before integration into one system

## Slide 14: Simulations: Polarized Patch Antenna
Sonnet or Momentum
Right Hand Circular Polarization
Modify linear patch antenna design to truncate corners.

## Slide 15: Simulations: Include Switches
Patches connected or not connected

## Slide 16: Double Stub Matching Network
A matching network allows maximum power transfer
Useable for most load admittances

## Slide 17: Double Stub Matching Network
Reconfigurable to match different patch resonant frequencies
Can not be analyzed until patch antenna system is designed
Methods:
  Using Smith Charts:
    Cancel out all imaginary impedances
    Match impedance to 50Ω
    Must be done for each patch (Reconfigurable)

## Slide 18: Task Schedule
Research (completed)
  Antenna Type
  Switching Device
  Polarization Methods
Simulations (in progress)
  Linear Patch Antenna
    1.575 GHz, 1.227 GHz
  Polarized Patch Antenna
  Determine Switch Parameters
  Polarized Patch Antenna w/ switches (on/off)

## Slide 19: Task Schedule (cont.)
Impedance Matching – Double Stub
  Smith Chart
  Stub Lengths
  Open or Short Circuit
Board Fabrication
  Microstrip Board
  Implement MEMS
  Switching Device

## Slide 20: Task Schedule (cont.)
Analysis
  Resonant Frequencies
  Efficiency
  Comparison to Simulation Results

## Slide 21: Tentative Remaining Schedule
Simulations – Purchasing of Parts
  Complete by end of Fall ’11 Semester
Impedance Matching
  Weeks 1-2
Fabrication
  Weeks 3-10
Analysis
  Weeks 11-15

## Slide 22: Questions?