## Slide 1
Closed Loop Control of Halbach Array Magnetic Levitation System Height
By: Kyle Gavelek
Victor Panek Christopher Smith
Advised by: Dr. Winfred Anakwa
Mr. Steven Gutschlag

## Slide 2
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Introduction
  Background
  CLCML Project
Development
  Planning
  Motor Model
  Controller
  Lookup Table
  Microcontroller
Conclusion
  Summarize Results
  Questions

## Slide 3: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Depiction of Halbach array implementation on high speed train
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion

## Slide 4: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Improve the rotational stability of the inductrack by balancing the wheel
Construct an enclosure in order to safely reach high rotational velocities
Model the DC motor and verify its accuracy to within +/- 5% of steady state
Designed a controller to achieve closed loop control of displacement height
Use a microcontroller to implement the controller
Objectives
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion

## Slide 5: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Last year’s final inductrack system
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion

## Slide 6: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Magnetic Field Lines
Sinusoidal Magnetic Field Generated
Br – Individual Magnet’s Strength d – Thickness of magnets
λ – wavelength M – # of magnets per wavelength
Halbach Array Theory
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
T

## Slide 7: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Velocity of Halbach Array’s Magnetic Field
Inductrack Properties
Inductrack Theory
Copper inductrack
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion

## Slide 8
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Excitation Frequency:
v – velocity of Halbach Array
k – wavenumber of Halbach Array’s magnetic field
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Inductrack Theory
RL Bode Phase Response

## Slide 9
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Excitation Frequency:
v – velocity of Halbach Array
k – wavenumber of Halbach Array’s magnetic field
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Inductrack Theory

## Slide 10: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Magnetic Flux:
[Wb]
w – width of Halbach Array k – wave number =2π/λ
ωe – excitation frequency = kv y – vertical distance
Peak Magnetic Flux:
[Wb]
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Halbach Array – Inductrack Interaction

## Slide 11
Induced Current:
[A]
Induced Voltage:
[V]
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Inductrack Properties:
R – inductrack resistance L – inductrack inductance
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Halbach Array – Inductrack Interaction

## Slide 12
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Vertical Force:
[N]
A – Area under the Halbach Array
dC – Spacing of Inductors
Halbach Array – Inductrack Interaction
Drag Force:
[N]

## Slide 13: Closed Loop Control of Halbach Array Magnetic Levitation System Height
RC – Resistivity of Copper
l – Length of Inductor circuit
A – Inductrack Cross-sectional Area
μ0 – Permeability of free space
λ – Wavelength of magnetic field
PC – Mean Perimeter of Inductrack circuit
dC – Spacing of Inductors
2011-2012 Calculated Parameters
B0 = 0.8060 T R = 1.9 x 10-4 Ω
L = 7.532 x 10-8 H
Inductrack Resistance:
Inductrack Inductance:
Peak Magnetic Field:
Revised Parameter Calculations
B0 = 0.8060 T R = 2.12 x 10-4 Ω
L = 6.86 x 10-8 H
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Ω
H

## Slide 14
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Last year’s final inductrack system
Inductrack System with safety enclosure
System Improvements

## Slide 15
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Notes: All Visio diagrams need to be redrawn

## Slide 16
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Motor Model Performance Specifications:
Steady State accuracy within +/- 5%
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Lookup Table Specifications:
Contain data points to allow a resolution of 0.5 mm
Controller Design Specifications:
Maximum overshoot less than 10%
Steady state error equal zero for unit step input
Minimize settling time based on other specifications
Notes: All Visio diagrams need to be redrawn

## Slide 17: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Common DC Motor Circuit Schematic
i
Parameters to determine:
Ra – armature resistance La – armature inductance
kv – motor torque constant kT – back emf constant
B – motor viscous friction Tcf – columbic friction
J – moment of inertia
Measurable Quantities:
ωm – machine rotational speed i – amature current
Va – source voltage Vb – back emf voltage
Motor Model Design Equations

## Slide 18: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Ra = 2.00 Ω
Determination of Armature Resistance
Common DC Motor Circuit Schematic
[V]
[Ω]
Va [V] | i [A] | Ra [Ω]
Digital Multimeter | Current Probe | R=Va/Ia
1.0 | 0.20 | 5.00
2.0 | 0.45 | 4.40
3.2 | 1.00 | 3.20
5.2 | 2.00 | 2.60
6.5 | 3.00 | 2.16
8.0 | 4.00 | 2.00
9.3 | 5.00 | 1.86
11.0 | 6.00 | 1.83

## Slide 19: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
ms
H
Determination of Armature Inductance
Common DC Motor Circuit Schematic

## Slide 20: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
 | Va [V] | ia [A] | ωm [RPM] | ωm [rad/s]
 | Digital Multimeter | Current Probe | Tachometer | [rad/s]= [RPM]*π/30
Trial 1: | 20.5 | 0.95 | 270 | 28.274
Trial 2: | 50.45 | 1.04 | 735 | 76.969
Average V/rad/s
N m/A
Determination of Back emf Constant and Motor Torque Constant
Common DC Motor Circuit Schematic
V/rad/s
V/rad/s

## Slide 21: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
i
 | ia [A] | ωm [RPM] | ωm [rad/s]
 | Current Probe | Tachometer | [rad/s]=RPM*π/30
Trial 1: | 1.038 | 200 | 20.93
Trial 2: | 1.350 | 735 | 76.93
B = 0.0061 N m/rad/s Tcf = 0.5105 N m
Determination of Viscous Friction and Coulombic Friction Torque

## Slide 22: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Determination of Moment of Inertia
Common DC Motor Circuit Schematic

## Slide 23: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
 | ω(0+)[RPM] | ω(0+)[rad/s] | t[sec] | Vb(t)[V]
 | Tachometer | [rad/s]=[RPM]*π/30 | Voltage Probe | Voltage Probe
Trial 1: | 498 | 52.15 | 0.20 | 26.0
 |  |  | 0.80 | 8.6
Trial 2: | 1010 | 105.77 | 0.40 | 52.6
 |  |  | 1.50 | 18.0
Average kg m2
Determination of Moment of Inertia
J1 = 0.2471 kg m2 J2 = 0.2920 kg m2
J3 = 0.2413 kg m2 J4 = 0.2603 kg m2

## Slide 24
Closed Loop Control of Halbach Array Magnetic Levitation System Height
24
Introduction
  Background
  CLCML Project
Development
  Planning
  Motor Model
  Controller
  Lookup Table
  Microcontroller
Conclusion
  Summarize Results
  Questions
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Notes: 24

## Slide 25: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
+
–
i
–
+

## Slide 26: Closed Loop Control of Halbach Array Magnetic Levitation System Height
  R = 2.00 Ω L = 0.0216 H
  kt = 0.615 Nm/A kv = 0.615 V/(rad/s)
  Tcf = 0.5105 N m B = 0.0061 Nm/(rad/s)
  J = 0.216 kg m2
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
+
–
–
+

## Slide 27: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Voltage | Velocity |  | 
Va (V) | Fenc (Hz) | vRPM (rpm) | ωm (rad/s)
7.15 | 5.600 | 84.000 | 8.792
8.32 | 6.800 | 102.000 | 10.676
9.76 | 8.100 | 121.500 | 12.717
11.15 | 9.500 | 142.500 | 14.915
13.00 | 11.300 | 169.500 | 17.741
14.65 | 12.800 | 192.000 | 20.096
16.85 | 15.200 | 228.000 | 23.864
20.34 | 19.000 | 285.000 | 29.830
24.95 | 23.800 | 357.000 | 37.366
30.29 | 28.700 | 430.500 | 45.059
35.71 | 34.500 | 517.500 | 54.165
40.60 | 39.900 | 598.500 | 62.643
45.35 | 45.000 | 675.000 | 70.650
49.96 | 49.000 | 735.000 | 76.930
54.86 | 54.750 | 821.250 | 85.958
59.92 | 60.000 | 900.000 | 94.200
64.70 | 65.000 | 975.000 | 102.050

## Slide 28: Closed Loop Control of Halbach Array Magnetic Levitation System Height
  Time (seconds)
  Rotational Velocity (rad/s)
  Green = Experimental Steady State Blue = Model Simulation
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion

## Slide 29: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Voltage | Velocity | SIMULINK Model | % Error
Va (V) | ωm (rad/s) | ωm (rad/s) | 
7.15 | 8.792 | 8.643 | -1.69%
8.32 | 10.676 | 10.490 | -1.75%
9.76 | 12.717 | 12.758 | 0.32%
11.15 | 14.915 | 14.947 | 0.22%
13.00 | 17.741 | 17.861 | 0.68%
14.65 | 20.096 | 20.460 | 1.81%
16.85 | 23.864 | 23.925 | 0.26%
20.34 | 29.830 | 29.421 | -1.37%
24.95 | 37.366 | 36.682 | -1.83%
30.29 | 45.059 | 45.092 | 0.07%
35.71 | 54.165 | 53.630 | -0.99%
40.60 | 62.643 | 61.333 | -2.09%
45.35 | 70.650 | 68.815 | -2.60%
49.96 | 76.930 | 76.077 | -1.11%
54.86 | 85.958 | 83.795 | -2.52%
59.92 | 94.200 | 91.765 | -2.58%
64.70 | 102.050 | 99.295 | -2.70%

## Slide 30
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Input Voltage
Va=9.65 V
Steady State Velocity
ωss=12.4 rad/s
Input Voltage
Va=20.6 V
Steady State Velocity
ωss=29.4 rad/s
Input Voltage
Va=39.5 V
Steady State Velocity
ωss=59.7 rad/s
Chart: Transient Response Initial Velocity: 12.4 [rad/s]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Experimental | 7.8 | 6 | 5 | 3.8 | 2.5 | 1.2 | 0.2 | 0.2 | 0.1
Theoretical | 7.6278 | 6.2841 | 4.971 | 3.6877 | 2.4336 | 1.208 | 0.010256 | 0 | 0
Chart: Transient Response Initial Velocity: 29.4 [rad/s]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Experimental | 18.2 | 16.8 | 15.6 | 13.9 | 12.8 | 11.3 | 9.8 | 8.7 | 7.4 | 5.9 | 4.7 | 3.5 | 2.2 | 1 | 0.2 | 0.2 | 0.1
Theoretical | 18.0558 | 16.475 | 14.9301 | 13.4204 | 11.945 | 10.5031 | 9.094 | 7.717 | 6.3713 | 5.0561 | 3.7709 | 2.5149 | 1.2874 | 0.087903 | 0 | 0 | 0
Chart: Transient Response Initial Velocity: 59.7 [rad/s]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Experimental | 36.4 | 34.2 | 32.4 | 30.6 | 29 | 27 | 25.4 | 24.2 | 21.8 | 20.4 | 18.8 | 17.6 | 15.8 | 14.2 | 12.2 | 11 | 9.4 | 7.8 | 6.6 | 5 | 3.8 | 2.8 | 1.4 | 0.2 | 0.2 | 0.1
Theoretical | 36.6909 | 34.6864 | 32.7274 | 30.813 | 28.9421 | 27.1138 | 25.327 | 23.5809 | 21.8745 | 20.2068 | 18.5771 | 16.9845 | 15.428 | 13.9069 | 12.4205 | 10.9678 | 9.5482 | 8.1608 | 6.805 | 5.48 | 4.1851 | 2.9197 | 1.683 | 0.4745 | 0 | 0
Chart: Transient Response Initial Velocity: 12.4 [rad/s]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Experimental | 7.8 | 6 | 5 | 3.8 | 2.5 | 1.2 | 0.2 | 0.2 | 0.1
Chart: Transient Response Initial Velocity: 29.4 [rad/s]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Experimental | 18.2 | 16.8 | 15.6 | 13.9 | 12.8 | 11.3 | 9.8 | 8.7 | 7.4 | 5.9 | 4.7 | 3.5 | 2.2 | 1 | 0.2 | 0.2 | 0.1
Chart: Transient Response Initial Velocity: 59.7 [rad/s]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Experimental | 36.4 | 34.2 | 32.4 | 30.6 | 29 | 27 | 25.4 | 24.2 | 21.8 | 20.4 | 18.8 | 17.6 | 15.8 | 14.2 | 12.2 | 11 | 9.4 | 7.8 | 6.6 | 5 | 3.8 | 2.8 | 1.4 | 0.2 | 0.2 | 0.1

## Slide 31
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
[rad/s] [rad/s]

## Slide 32
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Design Specification 1: Steady State Error = 0 for unit step input
Controller Transfer Function will have an integrator.
Design Specification 2: Less than 10% Overshoot
Damping Ratio: ζ = 0.707
Design Specification 3: Settling Time less than 4 second
Settling Time: ts < 4 seconds
[rad/s] [rad/s]

## Slide 33
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Design Specification 1: steady state error = 0
Design Specification 2: Less than 10% overshoot. ζ = 0.707
Design Specification 3: ts < 4 seconds

## Slide 34
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Design Specification 1: steady state error = 0
Design Specification 2: Less than 10% overshoot. ζ = 0.707
Design Specification 3: ts < 4 seconds

## Slide 35
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Controller Transfer Function:
A more realistic Transfer Function:
A lead network with integral action.

## Slide 36
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height

## Slide 37
Green = Controller Blue = Uncontrolled
  Time (seconds)
  Rotational Velocity (rad/s)
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
ωss = 44.65
ωpeak = 48.41
0.95ωss = 42.42
1.05ωss = 46.88
.
.
.

## Slide 38
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
+
–
Desired Rotational Velocity
Resulting Rotational Velocity
Determination of Sampling Time

## Slide 39
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
sec
Determination of Sampling Time

## Slide 40
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Closed Loop Control of Halbach Array Magnetic Levitation System Height
Continuous Time Controller:
Discrete Time Controller:
sec
Difference Equation form:
Digital Controller Design

## Slide 41: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Chart: Force Sensor Data Starting Height 8.0 [mm]
| 0 | 40.5 | 95.4 | 151.95000000000002 | 210 | 270 | 337.04999999999995 | 417 | 487.5 | 574.5 | 648.9 | 762 | 859.5 | 940.5 | 1001.55 | 1107 | 1185 | 1253.4000000000001 | 1344.4499999999998
Experimental | 0 | 0.55 | 1.56 | 3 | 4.6 | 6 | 7.8 | 9.3 | 10.9 | 12.2 | 13.23 | 14.65 | 15.5 | 16.45 | 17.18 | 17.94 | 18.65 | 19.4 | 20.16
Theoretical | 0 | 0.14421 | 0.78265 | 1.9071 | 3.4388 | 5.2795 | 7.4745 | 10.0757 | 12.2272 | 14.6084 | 16.3824 | 18.6378 | 20.209 | 21.2958 | 22.0045 | 23.0424 | 23.6841 | 24.174 | 24.7378
Chart: Force Sensor Data Starting Height 7.0 [mm]
| 40.5 | 67.5 | 82.5 | 105 | 121.5 | 144.75 | 171.3 | 174.9 | 183 | 190.95000000000002 | 198 | 213 | 249.00000000000003 | 292.5 | 330 | 385.2 | 445.5 | 506.25 | 541.65 | 600 | 705 | 780 | 870 | 967.5 | 1080
Experimental | 0.5 | 1.15 | 1.6 | 2.2 | 2.75 | 3.5 | 4.1 | 4.35 | 4.51 | 4.75 | 4.9 | 5.4 | 6.33 | 7.4 | 8.35 | 9.31 | 10.32 | 11.17 | 11.81 | 12.43 | 13.5 | 14.19 | 14.8 | 15.6 | 16.24
Theoretical | 0.2259 | 0.62205 | 0.92306 | 1.4768 | 1.956 | 2.7274 | 3.7309 | 3.8759 | 4.2095 | 4.5462 | 4.8519 | 5.5229 | 7.2284 | 9.411 | 11.3435 | 14.1838 | 17.1781 | 19.9997 | 21.5349 | 23.8783 | 27.5133 | 29.6869 | 31.8929 | 33.8662 | 35.7097

## Slide 42: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
N
Chart: Displament Sensor Data Starting Height = 7.0 mm
| 31.5 | 84 | 93 | 103.5 | 112.5 | 126 | 136.5 | 147 | 175.5 | 196.5 | 225 | 249.00000000000003 | 277.5 | 375 | 465 | 540 | 630 | 705 | 780 | 855 | 945 | 1020 | 1095 | 1185 | 1260 | 1350 | 1425 | 1500 | 1575 | 1650 | 1725
Experiemental | 7 | 7.0102 | 7.082 | 7.1844 | 7.2459 | 7.3483 | 7.4508 | 7.5737 | 7.6864 | 7.8708 | 8.2089 | 8.3728 | 8.5572 | 9.6124 | 10.1656 | 10.6881 | 10.975 | 11.2618 | 11.4872 | 11.6204 | 11.7638 | 11.9175 | 12.0097 | 12.1429 | 12.2761 | 12.3683 | 12.4605 | 12.5732 | 12.6859 | 12.7678 | 12.8498
Theoretical | -0.80887 | 3.5214 | 3.9644 | 4.4276 | 4.7865 | 5.2707 | 5.6098 | 5.9211 | 6.6534 | 7.1094 | 7.6417 | 8.0278 | 8.4272 | 9.4461 | 10.0733 | 10.4521 | 10.7908 | 11.0049 | 11.1742 | 11.3099 | 11.4396 | 11.5266 | 11.5989 | 11.6704 | 11.7201 | 11.7702 | 11.8055 | 11.8362 | 11.8629 | 11.8863 | 11.907

## Slide 43
Closed Loop Control of Halbach Array Magnetic Levitation System Height
43
Introduction
  Background
  CLCML Project
Development
  Planning
  Motor Model
  Controller
  Lookup Table
  Microcontroller
Conclusion
  Summarize Results
  Questions
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Notes: 43

## Slide 44: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Motor – μController Interface
Vs
Displacement Sensor
Optical Encoder
User Input
PWM
uController
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Power
MOSFET

## Slide 45: Closed Loop Control of Halbach Array Magnetic Levitation System Height
To Motor
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
To Motor
Vs = 80 V
+5 V
PWM from microcontroller

## Slide 46: Closed Loop Control of Halbach Array Magnetic Levitation System Height
uController
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
  uController Inputs:
    User Input: Desired Displacement
    Optical Encoder: Current Speed
    Displacement Sensor: Resulting Displacement

## Slide 47: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Funtions of the STR2NUM function:
  Stores user input as characters in array
  Converts char stored in array to int data type
  Ones value input > 6 is reverted to 6
  Decimal value input rounded down to 0 or 5.
  Stores final integer result in VALUE to be used in PWM.

## Slide 48: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
y
Functions of CONTROLLER:
  Calculate velocity error
  Output voltage calculated using difference equation (shown below)
  Store previous voltage and velocity error values for next iteration

## Slide 49: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Functions of PWM:
  Read duty cycle (DC) % from VALUE
  Set TH0 and TL0 based on DC %
  Set P4.4 output
  Reset on Timer 0 overflow
  The high and low portions of the PWM signal both follow this procedure to produce the proper output.

## Slide 50: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
PWM Outputs from microcontroller
Ch 1: PWM Output Ch 2: Vs
Ch 3: Drain Vtg Ch 4: Source Current
MATH: Ch 2 – Ch 3 = Motor Vtg
~ 25% Duty Cycle ~ 50% Duty Cycle

## Slide 51: Closed Loop Control of Halbach Array Magnetic Levitation System Height
51
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion
Improve the rotational stability of
the inductrack by balancing the
wheel
Construct an enclosure in order to
safely reach high rotational
velocities
Model the DC motor and verify its
accuracy to within +/- 5% of steady
state
Designed a controller to achieve
closed loop control of displacement
height
Use a microcontroller to implement
the controller
Wheel has been balanced to within 2g
Safety enclosure designed and built in Jobst shop
Modelled DC motor within +/- 3% of steady state
values for rotational velocity up to 1000 RPM
Designed continuous time controller to achieve
closed loop control of rotational velocity
Converted controller to discrete time. Formed
difference equation to be used in microcontroller
Programmed microcontroller to accept user input
within range of operation (0 to 6.0 mm)
Successfully provide accurate PWM output using the
microcontroller
Collected displacement data and created lookup table
for starting displacement of 7.0 mm
Built and tested PWM circuit

## Slide 52: Closed Loop Control of Halbach Array Magnetic Levitation System Height
Richard F. Post
Magnetic Levitation System for Moving Objects
U.S. Patent 5,722,326
March 3, 1998
Richard F. Post
Inductrack Magnet Configuration
U.S. Patent 6,633,217 B2
October 14, 2003
Richard F. Post
Inductrack Configuration
U.S. Patent 629,503 B2
October 7, 2003
Richard F. Post
Laminated Track Design for Inductrack Maglev System
U.S. Patent Pending US 2003/0112105 A1
June 19, 2003
Coffey; Howard T.
Propulsion and stabilization for magnetically levitated vehicles
U.S. Patent 5,222,436
June 29, 2003
Coffey; Howard T.
Magnetic Levitation configuration incorporating levitation,
guidance and linear synchronous motor
U.S. Patent 5,253,592
October 19, 1993
Levi;Enrico; Zabar;Zivan
Air cored, linear induction motor for magnetically levitated
systems
U.S. Patent 5,270,593
November 10, 1992
Lamb; Karl J. ; Merrill; Toby ; Gossage; Scott D. ; Sparks;
Michael T. ;Barrett; Michael S.
U.S. Patent 6,510,799
January 28, 2003
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion

## Slide 53: Closed Loop Control of Halbach Array Magnetic Levitation System Height
[1] Dirk DeDecker, Jesse VanIseghem. Senior Project. “Development of a Halback Array Magnetic Levitation System”. Final Report, May 2012
[2] Glenn Zomchek. Senior Project. “Redesign of a Rotary Inductrack for Magnetic Levitation Train Demonstration.” Final Report, 2007.
[3] Paul Friend. Senior Project. Magnetic Levitation Technology 1. Final Report, 2004.
[4] Post, Richard F., Ryutov, Dmitri D., “The Inductrack Approach to Magnetic Levitation,” Lawrence Livermore National Laboratory.
[5] Post, Richard F., Ryutov, Dmitri D., “The Inductrack: A Simpler Approach to Magnetic Levitaiton,” Lawrence Livermore National Laboratory.
[6] Post, Richard F., Sam Gurol, and Bob Baldi. "The General Atomics Low Speed Urban Maglev Technology Development Program." Lawrence Livermore National Laboratory and General Atomics.
Background
CLCML Project
Planning
Motor Model
Controller
Lookup Table
μController
Conclusion