## Slide 1: Ultrasound Simulations using REC and SAFT
Presenter:
Tony Podkowa
November 13, 2012
Advisor: Dr José R. Sánchez
Department of Electrical and Computer Engineering

## Slide 2: Outline
I. Introduction
II. Project Summary
III. Block Diagram
IV. Preliminary Work
V. Schedule

## Slide 3: Outline
I. Introduction
II. Project Summary
III. Block Diagram
IV. Preliminary Work
V. Schedule

## Slide 4: Introduction
Medical Applications
  Tumor detection
  Blood flow imaging
  Cardiac imaging
Piezoelectric Transducer
  Ultrasonic Pulses
  Tissue Density reflects Pulses

## Slide 5: Outline
I. Introduction
II. Project Summary
III. Block Diagram
IV. Preliminary Work
V. Schedule

## Slide 6: Project Summary
Specialized techniques improve image resolution and SNR.
Resolution Enhancement Compression (REC)
  Improves Axial Resolution and SNR
Synthetic Aperture Focusing Techniques (SAFT)
  Improve Lateral Resolution and SNR
Goal:
To simulate the combination of both REC and SAFT in an ultrasound system using the Matlab addon Field II.

## Slide 7: Outline
I. Introduction
II. Project Summary
III. Block Diagram
IV. Preliminary Work
V. Schedule

## Slide 8: System Block Diagram
REC
Transducer
SAFT
Vin(t)
Vpc(t)
Image
Recon.
Image Output
Vlc(t)
Received Echo Signals
Beamformed Signals

## Slide 9: Resolution Enhancement Compression
Pulse Compression Technique
Uses Convolution Equivalence
Exchange the transducer impulse response a desired response
Increases bandwidth
Better resolution

## Slide 10
Source:
M. Oelze, “Bandwidth and Resolution Enhancement through Pulse Compression,” IEEE Trans. Ultrason., Ferroelec. and Freq. Control, vol. 54, pp. 768–781, Apr. 2007.

## Slide 11: REC Subsystem
Waveform
Generator
Vulc(f)
Vpc(f)
Tukey
Window
Vlc(f)
Vupc(f)

## Slide 12: System Block Diagram
REC
Transducer
SAFT
Vin(t)
Vpc(t)
Image
Recon.
Image Output
Vlc(t)
Received Echo Signals
Beamformed Signals

## Slide 13: Transducer
Linear Array Transducer consisting of several elements
Capable of emitting and receiving ultrasonic pulses
Generates several signals to be processed to form an image.
S. I. Nikolov, Synthetic Aperture Tissue and Flow Ultrasound Imaging. PhD thesis, Technical University of Denmark, Aug. 2001.

## Slide 14: Transducer Specifications
256 Elements
3 MHz Center Frequency
200 MHz Sampling Frequency
4 mm Element Height
0.26 mm Element Width
0.04 mm Element Kerf
20 mm Focus
Height
Width
Kerf

## Slide 15: System Block Diagram
REC
Transducer
SAFT
Received Echo Signals
Vin(t)
Vpc(t)
Image
Recon.
Beamformed Signals
Image Output
Vlc(t)

## Slide 16: Synthetic Aperture Focusing Techniques
Electrically focuses signals to create an artificial aperture.
Uses different excitation schemes
Three Variations:
  Generic Synthetic Aperture Ultrasound (GSAU)
  Synthetic Transmit Aperture Ultrasound (STAU)
  Synthetic Receive Aperture Ultrasound (SRAU)
Results generated by delay and sum beamforming.

## Slide 17: GSAU
Transmit with one and receive with one.
Each transmit event generates a low resolution image.
Information needs to be delayed appropriately for each pixel before summing.
Gain in SNR:

## Slide 18: STAU
Transmit with one and receive with all.
Additional degree of freedom
Gain in SNR:

## Slide 19: SRAU
Transmit with all and receive with one.
Gain in SNR:

## Slide 20: SAFT
Delay and Sum
Beamforming
Apodization
Image Scan Lines
Received Echo Signals

## Slide 21: Apodization
Spatial Windowing
Used to shape the beam profile
Reweighting by apodization coefficients
Several different windowing techniques can be studied
  Rectangular
  Triangular
  Raised Cosine
a1
a2
aN

## Slide 22: System Block Diagram
REC
Transducer
SAFT
Received Echo Signals
Vin(t)
Vpc(t)
Image
Recon.
Beamformed Signals
Image Output
Vlc(t)

## Slide 23: Image Reconstruction Subsystem
Wiener
Filter
Envelope
Detection
Logarithmic
Compression
Limiter
Beamformed Signal
Image Scan Line
Vlc(t)

## Slide 24: Outline
I. Introduction
II. Project Summary
III. Block Diagram
IV. Preliminary Work
V. Schedule

## Slide 25: Preliminary Work
Image Reconstruction subsystem completed.
STAU partially completed
  Conventional pulsing instead of REC
  Individual low resolution images generated.
  Output image generated.
  Rectangular apodization
  64 elements instead of 256

## Slide 26: Individual STAU Images

## Slide 27: Effect of Beamforming

## Slide 28: Outline
I. Introduction
II. Project Summary
III. Block Diagram
IV. Preliminary Work
V. Schedule

## Slide 29: Schedule
1/28 – 2/8: REC
2/11 – 2/22: GPGPU implementation of STAU
2/25 – 3/8: GSAU
3/11 – 3/29: SRAU
4/1 – 4/12: Prepare for Student Scholarship Expo
4/15 – 4/19: Expo
4/22 – 5/3: Write Final Report & Presentation

## Slide 30: Ultrasound Simulations using REC and SAFT
Presenter:
Tony Podkowa
November 13, 2012
Advisor: Dr José R. Sánchez
Department of Electrical and Computer Engineering

## Slide 31: Generic Synthetic Aperture Ultrasound
Object

## Slide 32: Generic Synthetic Aperture Ultrasound
Object

## Slide 33: Matched Filter
ADC
Pre-
amplifier
Matched
filter
Echo Signal
SAFT
A
Reconstructed image
A