## Slide 1: eGROW Plant Monitoring System
Adam Holler, Clay McKinley – Students
Dr. Alexander Malinowski – Advisor

## Slide 2: Outline
Problem Statement
Functional Requirements
Prior Work
Flowchart/Specifications
Operational Modes
Engineering Efforts
Parts Ordered/Current Inventory
Schedule/Division of Labor

## Slide 3: Problem Statement
Home automation is a growing market with products related to security, lighting, temperature control, etc…
Solutions for monitoring of house plants and small green-houses are only available on an industrial level
We aim to cure the common problem of helping users remember to care for their plants

## Slide 4: Functional Requirements
Features
  Long battery life
  Moisture
  Temperature
  Sunlight
  Weekly Updates (text, email)
  Alarms (plus battery alert)
  Battery Upgrade
  “Anytime+” Values
  Mobile Phone App
  Adam & Clay Water+ Emergency Drop
  Sound Alarm
Using a modified TI Sensor Tags which will be mounted in each pot
Sensors will read ambient temperature, humidity, light, tip-over detection, soil moisture
Sensors will be able to work indoors and outdoors
Battery life for the sensors must be sufficient enough to not be a burden (Several months+)
Sensors will transmit data to a cloud via ZigBee to an Ethernet gateway
Users will be able to monitor data and receive alerts on a smartphone app

## Slide 5: Review of Literature/Prior Work
Research into communication protocols: Bluetooth Low Energy & ZigBee vs Wi-Fi, 6LoWPAN, etc…
Research into other solutions similar to our project

## Slide 6
Block Diagram for our System

## Slide 7: Specifications
TI Sensor Tag (CC2650 wireless MCU)
  10 low-power sensors, including ambient light, digital microphone, magnetic sensor, humidity, pressure, accelerometer, gyroscope, magnetometer, object temperature and ambient temperature.
  Ultra low power, coin cell battery, ARM Cortex-M3.
  Uses Zigbee or 6LoWPAN.
Capacitive Soil Moisture Sensor v1.2
  5V, Analog readings 2.4-4.4V
Digi XBee® Gateway
  Protocols: UDP/TCP, DHCP. Security: SSL tunnels, WEP-40, WEP-104, WPA/WPA2, Authentication with PSK and EAP
  OS: Digi Embedded Linux

## Slide 8: Operational Modes
Sensors
  Awake
    Gather data
    Send data to ZigBee/Ethernet converter
  Sleep
    Sensor waits a specified amount of time before waking up to transmit again
ZigBee/Ethernet
  Receive data from sensors, upload to cloud via Ethernet.
App
  Read data from cloud to display for user

## Slide 9: Engineering Efforts
Tested Capacitive Moisture Sensor
Notes: 2.72 – 4.2 V range
No datasheet so
Will order more once confident with sensor
Also pin size wonky?
Water in lab problem

## Slide 10: Engineering Efforts
Installed DevPack on TI Sensor Tag
TI Smart Tag App
Installed Code Compiler Studio (took some time)
Read through documentation to program TI Sensor Tags
Read through documentation for Digi Gateway
Notes: BLE Device Manager
Renamed devices with app
Yes trying to figure out GPIO pins for use or whatever

## Slide 11: Parts Ordered and Inventory
4x BLUETOOTH SENSOR TAG * 296-38831-ND
3x DEBUGGER FOR SENSORTAG * 296-42039-ND
1x Networking Modules XBee Gateway ZigBee to Ethernet Intl * 888-X2E-Z3C-E1-W (came with ethernet cable)
1x Capacitive soil moisture sensor (plan to get more later)
Micro USB cables, Personal Computers

## Slide 12: Schedule and Division of Labor
Timeline:
  November/December/January - Start programming TI Tags and enable firmware for Zigbee
  February - Work on Zigbee Networking (and continue programming)
  March - Work on App, Alarms, and Cloud
  April - Continue development and wrap up work
  May - Finish final paper and presentation
Division of Labor
  Right now, we are still discovering, so we are working together. Once we get a grip on some things (and now we have multiple debuggers) we can start working separately.

## Slide 13: Citations
[1] J. Lee, Y. Su and C. Shen, "A Comparative Study of Wireless Protocols: Bluetooth, UWB, ZigBee, and Wi-Fi," IECON 2007 - 33rd Annual Conference of the IEEE Industrial Electronics Society, Taipei, 2007, pp. 46-51.
[2] swrr134c.pdf CC2650 SensorTag Texas Instruments